## Slide 1: STORMWATER RUNOFF

## Slide 2: WHAT IS STORMWATER RUNOFF?
Stormwater
  Water created by precipitation events, such as rainfall or snowmelt
Runoff
  Water that does not infiltrate into the ground
  Flows over land and impervious surfaces
    Impervious surfaces: Surfaces that do not allow stormwater to percolate through the soils below them

## Slide 3: RUNOFF AND WATER QUALITY
Non-point pollution
  Excess nutrients
    Nitrogen & phosphorous
  Litter
    Plastic bottles, wrappers, etc.
  Bacteria
    From animal & human waste
  Sediment
  Pesticides
  Metals
  Petroleum products
    Leaking vehicles
Source: https://www.usgs.gov/special-topic/water-science-school/science/runoff-surface-and-overland-water-runoff?qt-science_center_objects=0#qt-science_center_objects

## Slide 4: RUNOFF AND WATER QUALITY
Flooding
  No where for water to go
Can be harmful to plants, animals, and people
Presque Isle State Park, Ferry Slip
Source: https://www.usgs.gov/special-topic/water-science-school/science/runoff-surface-and-overland-water-runoff?qt-science_center_objects=0#qt-science_center_objects

## Slide 5: STORMWATER RUNOFF
Meteorological Factors
Type of precipitation
  Rain, snow, etc.
Rainfall intensity
Rainfall amount
Rainfall duration
Distribution of rainfall
  One watershed or many
Storm movement
Soil moisture
Physical Factors
Impervious & pervious surfaces
Land use
Vegetation
Soil type
  Sand, clay, etc.
Drainage area
Slope
Topography
Surface water bodies
  Lakes, streams, reservoirs, etc.
Source: https://www.usgs.gov/special-topic/water-science-school/science/runoff-surface-and-overland-water-runoff?qt-science_center_objects=0#qt-science_center_objects

## Slide 6: IMPERVIOUS SURFACES
Impervious
Roads
Parking lots
Driveways
Rooftops
Compacted soils
  Lawns
  Construction sites
Source: https://eriecountypa.gov/departments/planning-and-community-development/resources/stormwater-information/

## Slide 7: PERVIOUS SURFACES
Pervious
Paver stones
Pervious concrete
Porous asphalt
Mulch
Sand
Silt
Clay
Noncompacted soils
  Lawns
Source: https://www.toaks.org/departments/public-works/sustainability/water/landscaping-and-lawns/pervious-surfaces

## Slide 8: BENEFITS OF PERVIOUS SURFACES
Recharge groundwater
  Allow water to reach and contribute to the water table
Filter out pollutants in the water
Reduce contamination of surface waters
  Rivers, lakes, streams, oceans
  Less runoff = less pollutants
Source: https://www.toaks.org/departments/public-works/sustainability/water/landscaping-and-lawns/pervious-surfaces

## Slide 9: BENEFITS OF PERVIOUS SURFACES
Reduce the heat island effect
  Impervious surfaces absorb more heat
    Considerably hotter
    Take more energy to cool
      Air conditioning
  Most pervious surfaces do not contribute to this problem
Reduce flooding
  Water is absorbed and cannot build up
Reduced erosion
  Less runoff
Source: https://www.toaks.org/departments/public-works/sustainability/water/landscaping-and-lawns/pervious-surfaces

## Slide 10: STORMWATER MANAGEMENT
Reduces or eliminates the negative impacts of runoff
Includes
  Controlling flooding
  Reducing erosion
  Improving water quality
Accomplished by implementing Best Management Practices (BMPs)
  Structural, vegetative, or managerial practices
  Used to treat, prevent, or reduce water pollution
Source: https://www.michigan.gov/documents/deq/ess-nps-savvy-bmp_209386_7.pdf

## Slide 11: BEST MANAGEMENT PRACTICES (BMPs)
Permeable surfaces
  Allows water to infiltrate pavement and enter soil
  Removes fine grain pollutants and provides erosion control
  Pervious pavement, pavers, etc.
Source: https://www.michigan.gov/documents/deq/ess-nps-savvy-bmp_209386_7.pdf

## Slide 12: BEST MANAGEMENT PRACTICES (BMPs)
Extended Detention Ponds
  Hold stormwater until pollutants settle to the bottom
  Water is released slowly into nearby water body
  Reduces flooding and pollution in system
Water pond/detention ponds
  Allow incoming runoff to replace existing pond water
  Pollutants settle to the bottom preventing from entering system
  Provides minimal flood protection
Infiltration basins
  Capture stormwater and allow it to filter back into the ground
  Can be clogged by coarse grained pollutants
Source: https://www.michigan.gov/documents/deq/ess-nps-savvy-bmp_209386_7.pdf

## Slide 13: BEST MANAGEMENT PRACTICES (BMPs)
Basins/swales/strips
  Improve water quality by filtering heavy metals, nutrients, suspended solids, oils and grease
  Reduce storm water volume by storing runoff
  Typically vegetated along the channel bottom and sides
Source: https://deq.utah.gov/water-quality/low-impact-development

## Slide 14: BEST MANAGEMENT PRACTICES (BMPs)
Rain Gardens
  Small-scale, shallow vegetated depressions that store and filter storm water or runoff from impervious surfaces
  Include compost-amended native soils planted with native trees, shrubs, plants and groundcovers
  Great for any location
Source: https://deq.utah.gov/water-quality/low-impact-development

## Slide 15: BEST MANAGEMENT PRACTICES (BMPs)
Green roofs
  Mitigate the effects of urbanization on water quality by filtering, absorbing or detaining rainfall
  Constructed of lightweight soil media including a drainage layer and impermeable membrane to protect the building structure
  Special plants that thrive in the harsh, dry, high temperatures of the roof and tolerate short, intense periods of rainfall
Source: https://deq.utah.gov/water-quality/low-impact-development

## Slide 16: BEST MANAGEMENT PRACTICES (BMPs)
Rain barrel
  Captures water runoff from impervious surfaces such as roof and stores it for later use
  Reduces the amount of runoff
  Conserves water and a source of free water
Source: https://www.epa.gov/soakuptherain/soak-rain-rain-barrels#:~:text=Rain%20barrels%20capture%20water%20from,for%20use%20in%20your%20landscape.

## Slide 17: Example of a stormwater friendly neighborhood
Source: https://deq.utah.gov/water-quality/low-impact-development

## Slide 18: STORMWATER BMPs IN ERIE, PA

## Slide 19: STORMWATER BMPs IN ERIE, PA

## Slide 20: IDENTIFYING IMPERVIOUS & PERVIOUS SURFACES
Answer each of the questions below for the following images
  Mostly pervious or impervious surfaces?
  How well does this area manage stormwater runoff?

## Slide 21: IDENTIFY PERVIOUS & IMPERVIOUS SURFACES IN THE IMAGE BELOW

## Slide 22: IDENTIFY PERVIOUS & IMPERVIOUS SURFACES IN THE IMAGE BELOW

## Slide 23
BROUGHT TO YOU BY…
THE REGIONAL SCIENCE
CONSORTIUM

## Slide 24
LEARN MORE AT…
www.RegSciConsort.com
www.RegSciTV.com